## Slide 1: CS534 Project Feature Extraction
Mingzhe Hu
Min Huang
Chenbin Huang

## Slide 2
Epilepsy is a serious neurological disorder with unique characteristics, tending of recurrent seizures.
The patients in this disease will experience a sudden breakdown or unusual activity in the brain which will last from seconds to a few minutes. This is dangerous because this situation will accompany with fractures, burns, and even death
To detect seizures, the electroencephalogram (EEG) is used to record the overall electrical activity of the brain in a waveform. These signals store important information about seizures
However, it is still difficult to obtain apparent difference in EEG activity between epileptic and non-epileptic seizures, so it is hard to predict when the patients will be attacked.

## Slide 3
In this project, we are trying to use machine learning to analyze EEG signal to predict epileptic seizure.
We plan to compare different models and evaluate their sensibility and accuracy of prediction to find the most suitable model.
Data are segmented every 10 minutes, and each segment has five fields which are:
data: the channel×signal matrix, the core data, usually is 16×(data length sec× sampling frequency).
data length sec: the time span of the data, usually is 600 seconds.
sampling frequency: the frequency of the signal; number of data per channel per second, usually is 399.6098 which is approximately 400 for dogs, but may vary in patients’ data.
channels: the names of 16 channels.
sequence: the number of the segment in one hour, range from 1 to 6.
Table 1: File Counts of Available Subjects in Seizure Prediction Data Set.

## Slide 4: EEG – 1s
FFT

## Slide 5: EEG
EEG tend to have low frequency (not sampling frequency) ^1
  “most commonly studied waveforms include delta (0.5 to 4Hz); theta (4 to 7Hz); alpha (8 to 12Hz); sigma (12 to 16Hz); beta (13 to 30Hz), and gamma (30–100 Hz).”
^1: Nayak CS, Anilkumar AC. EEG Normal Waveforms. [Updated 2021 Jul 31]. In: StatPearls [Internet]. Treasure Island (FL): StatPearls Publishing; 2021 Jan-. Available from: https://www.ncbi.nlm.nih.gov/books/NBK539805/
Figure From: https://raphaelvallat.com/bandpower.html

## Slide 6: Detect - 1s
Ictal example
Interictal example

## Slide 7: Feature extraction
According to Michael Hills 1
  “FFT magnitudes in the low frequency range 1 to 47Hz ”
  “The range 1-47Hz was chosen through trial and error while attempting dimensionality- reduction. ”
Selection between Channels?
  Any useful information in positions?
    different weights？
    Or ...
1: https://github.com/MichaelHills/seizure-detection
Figure from Al-Fahoum AS, Al-Fraihat AA. Methods of EEG signal features extraction using linear analysis in frequency and time-frequency domains. ISRN Neurosci. 2014;2014:730218. Published 2014 Feb 13. doi:10.1155/2014/730218

## Slide 8: Feature Extraction Across Channels
research 1 suggests that the coefficients of correlation in time domain and eigenvectors can be used to detect seizures.
  the correlation and eigenvectors from extracted low freq data in frequency domain.
  the correlation and eigenvectors from time domain.
Features:
low frequency FFT result
eigenvectors of corr in frequency domain
eigenvectors of corr in time domain
Schindler K, Leung H, Elger CE, Lehnertz K. Assessing seizure dynamics by analysing the correlation structure of multichannel intracranial EEG. Brain. 2007 Jan;130(Pt 1):65-77. doi: 10.1093/brain/awl304. Epub 2006 Nov 1. PMID: 17082199.

## Slide 9: Predict – fft - 600s
Preictal example
Interictal example
Notes: for some reason we don’t know the fft result is highly symmetrical

## Slide 10: feature extraction on long data
too many data in low frequency band
calculate band power
  power spectral density
  Welch’s Method1
Other summary features
maybe use same features for
the detection problem
1: Welch, P. D. (1967), "The use of Fast Fourier Transform for the estimation of power spectra: A method based on time averaging over short, modified periodograms" (PDF), IEEE Transactions on Audio and Electroacoustics, AU-15 (2): 70–73, Bibcode:1967ITAE...15...70W, doi:10.1109/TAU.1967.1161901
Figure from: https://github.com/garethjns/Kaggle-EEG

## Slide 11: Other details to be determined
after feature extraction, data dimension is still high
  windows for time selection
the selection of the frequency?
  divide frequencies into different bands